## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Fall 2019
Embedded Systems
Lab 2
Analog-to-Digital Converter (ADC)

## Slide 2: Analog-to-Digital Converter (ADC)
ADC is important almost to all application fields
Converts a continuous-time voltage signal within a given range to discrete-time digital values to quantify the voltage’s amplitudes
x(t)
quantize
x(n)
continuous-time analog signal
discrete-time digital values
ADC

## Slide 3: Analog-to-Digital Converter (ADC)
Three performance parameters:
  sampling rate
  resolution
  power dissipation
Many ADC implementations:
  sigma-delta
  successive-approximation
  pipeline

## Slide 4: Resolution
Resolution is determined by number of bits (in binary) to represent an analog input.
Example of two quantization methods (N = 3)
½ Δ
Δ
Max quantization error = Δ = VREF/23
Max quantization error = ±½ Δ = ±VREF/24

## Slide 5: Quantization Error
For N-bit ADC, it is limited to ±½Δ
Δ = is the step size of the converter.
Example: for 12-bit ADC and input voltage range [0, 3V]
Δ

## Slide 6: Minimum Sampling Rate: Nyquist–Shannon Sampling Theorem
In order to be able to reconstruct the analog input signal, the sampling rate should be at least twice the maximum frequency component contained in the input signal
Example of two sine waves have the same sampling values. This is called aliasing.
from wiki.com
Antialiasing (beyond the scope of this course)
  Pre-filtering: use analog hardware to filtering out high-frequency components and only sampling the low-frequency components. The high-frequency components are ignored.
  Post-filtering: Oversample continuous signal, then use software to filter out high-frequency components

## Slide 7: Successive-approximation (SAR) ADC

## Slide 8: Determining Minimum Sampling Time
Larger sampling time
Smaller sampling error
Slower ADC speed
Tradeoff
Sampling time is software programmable!

## Slide 9: Programming ADC Sampling Time
Prescaler
/1, /2, /4
HSI Clock
16 MHz
ADC Clock
4 cycles
9 cycles
16 cycles
24 cycles
48 cycles
96 cycles
192 cycles
384 cycles
Selection
ADC sample time register (SMPR)
default prescaler = 1

## Slide 10: Successive-approximation (SAR) ADC
Binary search algorithm to gradually approaches the input voltage
Settle into ±½ LSB bound within the time allowed
is software configurable

## Slide 11: ADC Conversion Time
Suppose ADCCLK = 16 MHz and Sampling time = 4 cycles
For 12-bit ADC
For 6-bit ADC

## Slide 12: Data Alignment

## Slide 13: ADC: Regular vs injected

## Slide 14: ADC Mode

## Slide 15: ADC Mode
Regular channel:
Set SWSTART in ADC_CR2
The channel is selected by SQ1[4:0] in SQR5
Result is stored in ADC_DR
EOC is set after conversion
Interrupt is generated if EOCIE is set
Injected channel:
Set JSWSTART in ADC_CR2
The channel is selected by JSQ1[4:0] in JSQR
Result is stored in ADC_JDR1
JEOC is set after conversion
Interrupt is generated if JEOCIE is set

## Slide 16: ADC Mode
Channels are selected by ADC_SQRx registers for regular channels, and by ADC_JSQR register for injected channel
All channels in a regular group share the same result register ADC_DR. Make sure to read data between consecutive sampling.

## Slide 17: VREF
Some chips does not expose VREF to a pin
  STM32L LQFP64 does not have VREF pin
  STM32L LQFP100 does
Infer internal VREF
  How?
Corresponds to

## Slide 18: Analog Watchdog
If V < VLTR or V > VHTR, the analog watchdog (AWD) flag (in ADC Status Register) is set, generating an interrupt to the processor
The monitor is automatically performed by hardware, not software
Convenient and efficient feature
Help processor detect exceptions and recover from specific situations
  For example, monitor sensor data and raise alarm on some level.
Analog voltage
Higher threshold (HTR)
Lower threshold (LTR)
Guarded Area
Two programmable thresholds

## Slide 19: Example: ADC with Timer Interrupts
ISR = Interrupt Service Routine
TIMER ISR starts ADC
ADC samples multiple channels
ADC ISR copies ADC data register to memory
Main program
ADC
Peripheral
ADC ISR
Timer
Peripheral
Set up timer
Timer ISR
timer interrupt
ADC interrupt
Set ADC_Done flag
Wait for DAC_Done = 1
Process Data
Repeat

## Slide 20: Example: ADC with Timer and DMA
Timer ISR starts ADC and DMA
DMA automatically copies ADC results of multiple channels to memory after each conversion
Main program
ADC
Peripheral
Timer
Peripheral
Set up timer
Timer ISR
timer interrupt
Set DMA_Done flag
Wait for DMA_Done = 1
Process Data
Repeat
DMA
Controller
Set up DMA
sampling
channels