## Slide 1: Teaching Embedded Systems with Drones
Sean Cashman, Steven Ferrarese, Atheer Oufi, Spencer Goulette, Yifeng Zhu
ASEE 2019
University of Maine
Marco De Fazio, Giorgio Mariano STMicroelectronics, Geneva, Switzerland

## Slide 2: Role of Embedded Systems: Lays foundation
ISA
DMA
FPU
Memory-mapped I/O
Interrupts
Arithmetic
Software Design
Embedded Systems
Computer Organization
decoding
numbers
debugging
communication
debugging
data structure
concurrency
Laying foundation in curriculum:
  Computer organization & architecture
  Operating systems
  Software design & algorithms
  Senior project design
Body of Knowledge (IEEE/ACM Computer Engineering Curricula 2016)
  Number systems and data encoding
  Instruction set architecture
  Relevant tools, standards and/or engineering constraints
  Input/output interfacing and communication
  Interrupts, timers, waveform generation
  Implementation strategies for complex embedded systems
  Computing platforms for embedded systems

## Slide 3: Teaching Embedded Systems with Drones: Overview
Textbook
ST Drone Kit, $50
Lab handout, solution, and presentation

## Slide 4: ST’s Mini Drone Kit

## Slide 5: Programming & Debugger
ST-LINK/V2, $23
STMicroelectronics NUCLEO, $10
or

## Slide 6: Textbook (Optional)
See a program running
Data representation
ARM instruction set architecture
Arithmetic and logic
Load and store
Branch and conditional execution
Structured programming
Subroutines
64-bit data processing
Mixing C and assembly
Interrupt
Fixed-point & floating-point arithmetic
Instruction encoding and decoding
General-purpose I/O
General-purpose timers
Stepper motor control
Liquid-crystal display (LCD)
Real-time clock (RTC)
Direct memory access (DMA)
Analog-to-digital converter (ADC)
Digital-to-analog converter (DAC)
Serial communication protocols
Multitasking
Digital signal processing
738 pages, $69.50
Complete instructor's resource:
  Lecture slides, quizzes and exams, tutorials, lab handouts and solutions (pre-lab, in-lab, and post-lab), solutions to end-of-chapter exercises
Bare-metal programming at the register level without using any API libraries
Line-by-line translation from C to ARM assembly
Strike the balance between theoretical foundations and technical practices
Using flowcharts as a reading guide for processor datasheets
Online YouTube tutorials (11.2K subscribers)

## Slide 7: YouTube Lectures & Tutorials
Short Lectures
  Why do we use Two's Complement?
  Carry and Borrow Flag
  Overflow Flag
  Pointer
  Memory Mapped I/O
  GPIO Output: Lighting up a LED
  GPIO Input: Interfacing a joystick
Tutorials
  Create a project in Keil v5
  Debugging in Keil v5
  Clock configuration of STM32L4 processors
  Printing messages via UART through ST-Link V2.1
  How to fix common errors?
  Timer: PWM output
  Interrupt Enable and Interrupt Priority
  Interrupts
  External Interrupts (EXTI)
  System Timer (SysTick)
  Booting process
  LCD
  Race Conditions
https://www.youtube.com/channel/UCY0sQ9hpSR6yZobt1qOv6DA/

## Slide 8: Adopted by 80+ universities in US & Canada

## Slide 9: Aircraft Principal Axes
z
x
y
from wikipedia
Notes: An aircraft in flight is free to rotate in three dimensions. Pitch, nose up or down, rotation about the y axis running from wing to wing. Roll, rotation about the x axis running from nose to tail. Yaw, nose left or right, rotation about the z axis running up and down.

## Slide 10: Quadcopter basics: flight control dynamics
FCU
Front direction
FCU: Flight Control Unit
M3
M1
M2
M4
Front Direction
FCU: Flight Control Unit
CW: Blue(-)/Red(+)
CCW: Black(-)/White(+)
Notes: Two sets of rotors rotates in opposite directions.

## Slide 11: Quadcopter basics: flight control dynamics
FCU
Front direction
FCU: Flight Control Unit
M3
M1
M2
M4
Notes: If all rotors are spinning at the same speed, with two sets of rotors rotate in opposite directions, the total torque is zero. So there is no need for a tail rotor like on conventional helicopters. If all the rotors were to spin in the same direction, it would result in a net Torque causing the complete Quad to rotate.

## Slide 12: Quadcopter basics: flight control dynamics
A quadcopter hovers or adjusts its altitude by applying equal thrust to all 4 rotors.
A quadcopter adjusts its yaw by applying more thrust to rotors rotating in the same direction.
A quadcopter adjusts its pitch or roll by applying more thrust to one rotor and less thrust to its diametrically opposite rotor.

## Slide 13: Bluetooth ST AppDrone
Button to connect to the Drone
Right joystick (ELE,AIL)
Left joystick(THR, RUD)
Yaw Right
Yaw Left
Throttle
High
Throttle
Low
Roll
Right
Roll
Left
Pitch
Down
Pitch
Up
https://github.com/STMicroelectronics-CentralLabs/ST_Drone_FCU_F401

## Slide 14: Alternate Remote Control

## Slide 15: Controller
LPS22HD
Pressure Sensor
LSM6DSL
A + G 6-axis IMU
LIS2MDL
Magnetometer
SPBTLE-RF
Bluetooth Smart v4.1 Module
40 mm
40 mm
STL6N3LLH6
Power MOSFET

## Slide 16: Controller

## Slide 17: Controller
M4
M2
M3
M1
32-bit MCU
A + G IMU
SPI2
Magnetometer
Power MOS x4
TIM4 PWM out
Remocon RX*
TIM2 input capture
Pressure Sensor
SPI1
STM32F401
LSM6DSL
LPS22HD
Battery charger
Micro USB **
LIS2MDL
I2C connector
4 x DC motor
LiPo 1-cell battery
BLE module
PWM
I2C2
SPBTLE-RF
UART connector
UART1
JTAG
JTAG connector
USB
STC4054
LDO
3V3
LD39015
P7
P3
P6
P1, P2, P4, P5
P8
BT1
CN1
STL6N3LLH6

## Slide 18: Teaching at which level?
Applications
Visual wizard tools (such as STMCubeMX)
HAL (Hardware Abstraction Layer) libraries
Bare-metal
Hardware
CMSIS-Core
HAL
CubeMX
Driver
Bare-metal: Bypass HAL and possibly CMSIS-Core

## Slide 19: HAL Level
; Initialize the Red LED pin (PB.2)
static GPIO_InitTypeDef GPIO_InitStruct;
GPIO_InitStruct.Mode = GPIO_MODE_OUTPUT_PP;
GPIO_InitStruct.Pull = GPIO_PULLUP;
GPIO_InitStruct.Speed = GPIO_SPEED_FREQ_VERY_HIGH;
GPIO_InitStruct.Pin = GPIO_PIN_2;
HAL_GPIO_Init(GPIOB, &GPIO_InitStruct);
HAL_GPIO_TogglePin(LED4_GPIO_PORT, LED4_PIN);
void HAL_GPIO_Init(GPIO_TypeDef *GPIOx, GPIO_InitTypeDef *GPIO_Init){
uint32_t position = 0x00;
uint32_t iocurrent = 0x00;
uint32_t temp = 0x00;
...
}
130
lines
Pros
  Simplify implementation
  Better portability
  Many examples
Cons
  Very complex to understand
  Cannot meet students’ curiosity

## Slide 20: Bare-Metal Level in C
#define LED_PIN 2
// GPIO Mode: Input(00), Output(01), AlterFunc(10), Analog(11, reset)
GPIOB->MODER &= ~(3<<(2*LED_PIN)); // Clear by using mask
GPIOB->MODER |= 1<<(2*LED_PIN); // Set as Output
// GPIO Speed: Low speed (00), Medium speed (01), Fast speed (10), High speed (11)
GPIOB->OSPEEDR &= ~(3<<(2*LED_PIN)); // Clear by using mask
GPIOB->OSPEEDR |= 2<<(2*LED_PIN); // Fast speed
// GPIO Output Type: Output push-pull (0, reset), Output open drain (1)
GPIOB->OTYPER &= ~(1<<LED_PIN); // Push-pull
// GPIO Push-Pull: No pull-up pull-down (00), Pull-up (01), Pull-down (10), Reserved (11)
GPIOB->PUPDR &= ~(3<<(2*LED_PIN)); // No pull-up, no pull-down
// Toggle up the LED
GPIOB->ODR ^= 1 << LED_PIN;
Only 7 lines of code
Focus on directly interfacing with hardware.
Do not use any libraries!

## Slide 21: Bare-Metal Level in Assembly
#define LED_PIN 2
// GPIO Mode: Input(00), Output(01), AlterFunc(10), Analog(11, reset)
GPIOB->MODER &= ~(3<<(2*LED_PIN));
GPIOB->MODER |= 1<<(2*LED_PIN); // Output(01)
LED_PIN EQU 2
LDR r0, =GPIOB_BASE
LDR r1, [r0, #GPIO_MODER]
EOR r1, r1, #(0x03<<(2*LED_PIN))
ORR r1, r1, #(1<<LED_PIN)
STR r1, [r0, #GPIO_MODER]
Set Pin B.2 as GPIO output
C implementation
Assembly implementation
Bare-metal level programming helps learning assembly programming
Translate naturally

## Slide 22: Eight lab modules for drones
Register-level Programming
  PWM output
  UART
  ADC
  SPI
Concept-level Understanding
  AHRS
  PID
  BLE
Application-level Programming
  Flying
USB Virtual COM
STM32Cube Hardware Abstraction Layer (HAL)
LSM6DSM
LISM2DL
STM32F4
LPS22HD
BLUENRG-MS
Remote Control
Flight Control
PID Control
AHRS
Development board
STEVAL-FCU001V1
HW components
Application
Middleware
Drivers
CMSIS
Utilities
Board Support Package
Components Support Package
Sensor Management
BLE stack
Module not yet implemented in current FW implementation
Motors
Each lab is independent from each other.

## Slide 23: Lab 1: PWM Output
Register-level programing a GPIO pin and a timer
Generate a PWM signal with fixed duty ratio and frequency
References:
  TrueStudio IDE installation tutorials
  Download TrueStudio Project from github
    Public students’ version
    Private teachers’ version
  Textbook
  STM32F401xC Reference Manual

## Slide 24: Lab 1: PWM Output
M4
M2
M3
M1
32-bit MCU
A + G IMU
SPI2
Magnetometer
Power MOS x4
TIM4 PWM out
Remocon RX*
TIM2 input capture
Pressure Sensor
SPI1
STM32F401
LSM6DSL
LPS22HD
Battery charger
Micro USB **
LIS2MDL
I2C connector
4 x DC motor
LiPo 1-cell battery
BLE module
PWM
I2C2
SPBTLE-RF
UART connector
UART1
JTAG
JTAG connector
USB
STC4054
LDO
3V3
LD39015
P7
P3
P6
P1, P2, P4, P5
P8
BT1
CN1
STL6N3LLH6

## Slide 25: Controller
CW: Blue(-)/Red(+)
CCW: Black(-)/White(+)
Motor control connector PWM signal on pin 2 (or P1, P2, P4, P5) with THR to min. value and to max. value
THR = Min
THR = Max

## Slide 26: Lab 1: PWM Output Pre-Lab

## Slide 27: Lab 1: PWM Output Lab coding & Demo
25% Duty Cycle, 494 Hz

## Slide 28: Lab 1: PWM Output Post-lab
Suppose the 16-MHz HSE (high-speed external clock) is selected as the input clock of timer 1. Answer the following questions and show your calculation process clearly. Write your answer in README.md and submit it to gitlab.
To generate 1 Hz square wave with a duty cycle of 50%, how should we set up the timer? Indicate your counting mode and show the value of ARR, CRR, and PSC registers.
What is the smallest PWM frequency that can be generated?

## Slide 29: Lab 2: UART
M4
M2
M3
M1
32-bit MCU
A + G IMU
SPI2
Magnetometer
Power MOS x4
TIM4 PWM out
Remocon RX*
TIM2 input capture
Pressure Sensor
SPI1
STM32F401
LSM6DSL
LPS22HD
Battery charger
Micro USB **
LIS2MDL
I2C connector
4 x DC motor
LiPo 1-cell battery
BLE module
PWM
I2C2
SPBTLE-RF
UART connector
UART1
JTAG
JTAG connector
USB
STC4054
LDO
3V3
LD39015
P7
P3
P6
P1, P2, P4, P5
P8
BT1
CN1
STL6N3LLH6

## Slide 30: Lab 2: UART Pre-lab
UART can be used to display debug information on PC
Register-level programming
USB to TTL Serial Cable

## Slide 31: Lab 2: UART
Basic Requirements:
  Polling for sending and receiving
For advanced courses
  Interrupts
  DMA
for (i = 0; i < nBytes; i++) {
// Wait until TXE (TX empty) is set
// Writing USART_DR automatically clears the TXE flag
while (!(USARTx->SR & USART_SR_TXE));
USARTx->DR = (buffer[i] & 0xFF);
}

## Slide 32: Lab 2: UART
Basic Requirements:
  Polling for sending and receiving
For advanced courses
  Interrupts
  DMA

## Slide 33: Lab 2: UART
Basic Requirements:
  Polling for sending and receiving
For advanced courses
  Interrupts
  DMA

## Slide 34: Lab 2: UART Post-lab
Using oscilloscope or digital analyzer or oscilloscope to analyze signals sent
1 start bit, 1 stop bit, 8 data bits, no parity, baud rate = 9600

## Slide 35: Lab 3: ADC
Measure battery voltage level
Send measurements to PC via UART
Independent of Lab 2
x(t)
quantize
x(n)
continuous-time analog signal
discrete-time digital values
ADC

## Slide 36: Lab 3: ADC
Basic Requirements:
  Constantly polling
  Polling with timer
Advanced
  Interrupts
  DMA
Wait for ready flag in ADC ISR
Process Data
Repeat
Main program

## Slide 37: Lab 3: ADC
Basic Requirements:
  Constantly polling
  Polling with timer
Advanced
  DMA
ISR = Interrupt Service Routine
TIMER ISR starts ADC
ADC samples multiple channels
ADC ISR copies ADC data register to memory
ADC
Peripheral
ADC ISR
Timer
Peripheral
Set up timer
Timer ISR
timer interrupt
ADC interrupt
Set ADC_Done flag
Wait for ADC_Done = 1
Process Data
Repeat
Main program

## Slide 38: Lab 3: ADC
Basic Requirements:
  Constant Polling
  Polling with timer
Advanced
  DMA
Timer ISR starts ADC and DMA
DMA automatically copies ADC results of multiple channels to memory after each conversion
Main program
ADC
Peripheral
Timer
Peripheral
Set up timer
Timer ISR
timer interrupt
Set DMA_Done flag
Wait for DMA_Done = 1
Process Data
Repeat
DMA
Controller
Set up DMA
sampling
channels

## Slide 39: Lab 4: SPI
M4
M2
M3
M1
32-bit MCU
A + G IMU
SPI2
Magnetometer
Power MOS x4
TIM4 PWM out
Remocon RX*
TIM2 input capture
Pressure Sensor
SPI1
STM32F401
LSM6DSL
LPS22HD
Battery charger
Micro USB **
LIS2MDL
I2C connector
4 x DC motor
LiPo 1-cell battery
BLE module
PWM
I2C2
SPBTLE-RF
UART connector
UART1
JTAG
JTAG connector
USB
STC4054
LDO
3V3
LD39015
P7
P3
P6
P1, P2, P4, P5
P8
BT1
CN1
STL6N3LLH6

## Slide 40: Lab 4 SPI
Sensor driver
  steval_fcu001_v1_accelero.c
  steval_fcu001_v1_gyro.c
  steval_fcu001_v1_magneto.c
  steval_fcu001_v1_pressure.c
Register-level programming assignments
  Sensor_IO_SPI_CS_Init_All(void)
  Sensor_IO_SPI_Init(void )
32-bit MCU
A + G IMU
SPI2
Magnetometer
Pressure Sensor
STM32F401
LSM6DSL
LPS22HD
LIS2MDL

## Slide 41: Lab 4 SPI
Lab Demo

## Slide 42: Lab 5: AHRS
Attitude and heading reference system (AHRS)
Conversion between Quaternions and Euler Angles
Calculate orientation of an object by using accelerometer and gyroscope
Notes: Euler angles are more human understandable and also good for decomposing rotations into individual degrees of freedom. Quaternions are more computationally efficient. You have to make three rotations and multiply them together when rotating by Euler angles, whereas a Quaternion is only one rotation and as it already encodes the sin and cos, the conversion from quaternion to matrix is quite efficient.
There's an ambiguity in the specification of Euler angles: which angle applies to which axis? Code that uses the convention (yaw, pitch, roll) won't interoperate with code that assumes (roll, pitch, yaw), and it may not be obvious, from looking at the code, which interpretation is being used.
Quaternions don't suffer from this ambiguity, since they only represent a single rotation, with a well-defined axis.

## Slide 43: Lab 5: AHRS
Sensor data updated
@800Hz
Low-pass filter
fc = 30Hz
Acc data
gyro data
Averaging every 5 samples
AHRS
@160Hz
Static calibration
IIR filter
FIFO_Order 5
Sensor_data.c
main.c
ahrs.c
Attitude and heading reference system (AHRS)
Conversion between Quaternions and Euler Angles
Calculate orientation of an object by using accelerometer and gyroscope
Pressure sensor and magnetometer are not used currently.

## Slide 44: Lab 5: AHRS
ψ/θ/Ф are the yaw/pitch/roll

## Slide 45: Lab 5: AHRS
  Accelerometer and gyroscope can calculate the attitude independently.
  Accelerometer is always influenced by high-frequency noise, and gyroscope has a low-frequency offset.
  Gyroscope results are accurate in short-term, but will generate an offset over time. Acc is not accurate in short-term because of noise, but is reliable over time.

## Slide 46: Lab 5: AHRS
Focus on understanding the concepts
  Conversion between Quaternions and Euler Angle
  Calculating the orientations by using gyroscope and accelerometer measurements
Example lab assignment
  Given constant gyroscope and accelerometer measurements
  Calculate and plot the orientation over the time

## Slide 47: Lab 6: PID

## Slide 48: Lab 6: PID
R/C
Receiver
Target Attitude
@50Hz
Sensor data updated
@800Hz
Low-pass filter
fc = 30Hz
Acc data
gyro data
Averaging every 5 samples
AHRS
@160Hz
PID outer loop
@160Hz
Static calibration
PID inner
Loop
@800Hz
M1 = Th – P – R + Y
M2 = Th + P – R – Y
M3 = Th + P + R + Y
M4 = Th – P + R – Y
Th = Thrust, P = Pitch
R = Roll, Y = Yaw
PWM generator
motors
Blocks in bolds are the Key ones for stabilization and anti-drifting.
IIR filter
FIFO_Order 5
Flightcontrol.c
rc.c
Sensor_data.c
Main.c
ahrs.c
Flightcontrol.c

## Slide 49: Lab 6: PID
PID control is performed in two separate stages:
PID Outer loop: comparing the target Euler angles given by Remocon and the Euler angles of the AHRS system, it controls the incline angle
PID Inner loop: used to track the angular rate.
Using a mathematical model of the drone system, it is almost impossible to make the system stable in a single loop. The inner loop has to be added to the outer loop in order to stabilize the system. The relative functions are present in flight_control.c:
+
PID
Outer loop
+
PID Inner loop
Pitch
Roll
+
-
+
-
Yaw
+

## Slide 50: Lab 6: PID
M1
M2
M3
M4
+
PID
Pitch
+
PID
Roll
+
PID
Yaw
Thrust
M1 = Thrust – PID_Pitch – PID_Roll + PID_Yaw
M2 = Thrust + PID_Pitch – PID_Roll – PID_Yaw
M3 = Thrust + PID_Pitch + PID_Roll + PID_Yaw
M4 = Thrust – PID_Pitch + PID_Roll – PID_Yaw

## Slide 51: Lab 6: PID
Study the impact of the PID control parameters to a drone in a restrained setting

## Slide 52: Lab 7: BLE
32-bit MCU
A + G IMU
SPI2
Magnetometer
Power MOS x4
TIM4 PWM out
Remocon RX*
TIM2 input capture
Pressure Sensor
SPI1
STM32F401
LSM6DSL
LPS22HD
Battery charger
Micro USB **
LIS2MDL
I2C connector
4 x DC motor
LiPo 1-cell battery
BLE module
PWM
I2C2
SPBTLE-RF
UART connector
UART1
JTAG
JTAG connector
USB
STC4054
LDO
3V3
LD39015
P7
P3
P6
P1, P2, P4, P5
P8
BT1
CN1
STL6N3LLH6
Notes: The is a single-mode Bluetooth low energy master/slave network processor module compliant with Bluetooth® v4.1.

## Slide 53: Lab 7: BLE
Generic Attribute Profile(GATT)
  defines how data is organized and exchanged
Attribute Protocol (ATT)
  allows the device to say what certain pieces of data are
  defined by a 16-bit universally unique identifier (UUID)
Security Manager(SM)
  encryption and authentication
Logical Link Control and Adaptation Protocol(L2CAP)
  encapsulate into the standard BLE packet format
Host Controller Interface(HCI)
Link Layer (LL)
Physical Layer(PHY)
GATT/ATT/SM
L2CAP
HCI
Host
SPI/UART/USB/SDIO
GATT/ATT/SM
L2CAP
HCI
Controller
Notes: A typical BLE system consists of an LE controller and a host. The LE controller consists of a physical layer (PHY) including the radio, a link layer (LL) and a standard host controller interface (HCI). The host consists of a HCI and other higher protocol layers, e.g. L2CAP, SM, ATT/GATT, GAP etc.
In many designs the LE controller and the host reside in two separate silicon chips and are controlled by 2 different microcontrollers. Communication between the two is transmitted via a hardware connection, e.g. UART, SPI, USB, etc. The host can send HCI commands to control the LE controller. The HCI interface and the HCI commands are standardized by the Bluetooth core specification. Please refer to the official document for more information.
Sometimes the LE controller and the host can be combined into a single chipset solution.

## Slide 54: Lab 7: BLE
User Application
Application Control Interface (ACI)
Host
Application Control Interface
(ACI)
BLE Protocol Stack
Radio Controller
BLE Controller
Power Management
Memory Management
SPI
Application Control Interface (ACI)
  User applications send ACI commands to control the BLE controller over SPI
  ACI commands utilize and extend the standard HCI data format.
    HCI command packet
    HCI ACL data packet
    HCI synchronous data packet
    HCI event packet

## Slide 55: Lab 7: BLE
tBleStatus Value_Update(uint16_t value1, int16_t value2) {
tBleStatus ret;
uint8_t BuffPos;
uint8_t buff[2+2+2]; //2 for tick value(2 bytes), 2 for value1(2 bytes), and 2 for value2(2 bytes)
STORE_LE_16(buff, (HAL_GetTick()>>3));
BuffPos=2;
STORE_LE_16(buff+BuffPos,value1);
BuffPos+=2;
STORE_LE_16(buff+BuffPos,value2);
BuffPos+=2;
ret = aci_gatt_update_char_value(HWServW2STHandle, EnvironmentalCharHandle, 0, 2+2+2,buff);//transmit data
if (ret != BLE_STATUS_SUCCESS){
return BLE_STATUS_ERROR;
}
return BLE_STATUS_SUCCESS;
}

## Slide 56: Lab 8: Simple drone control

## Slide 57: Lab 8: Simple drone control

## Slide 58: Lab 8: Simple drone control

## Slide 59: Summary
Lab Materials
  Lab description
  Lab presentation
  Lab starting code for students
  Lab solutions for instructors
Eight lab modules:
  Register-level Programming
    PWM output
    UART
    ADC
    SPI
  Concept-level Understanding
    AHRS
    PID
    BLE
  Application-level Programming
    Flying

## Slide 60: UAS Policy on Campus
Standard Operating Procedure for the Use of Unmanned Aerial Systems (UAS) on campus
  Make sure you have to compliance with the procedure if it exists
  It was simple for us for the ST drone kit. It was passed without formal applications and reviews.
  But always check with your safety and environment management office

## Slide 61: For more information
Send email to Yifeng.Zhu@maine.edu for
  An exam copy of my book
  Complete instructor resources: slides, exams, quizzes, solutions, lab handouts & solutions
My book website: http://web.eece.maine.edu/~zhu/book/
  Sample labs, lab kit, FAQ
My YouTube Channel: https://www.youtube.com/channel/UCY0sQ9hpSR6yZobt1qOv6DA
Thank STMicroelectronics for organizing and sponsoring this workshop!