## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Fall 2019
Embedded Systems
Lab 1
Timers and PWM

## Slide 2: Timer
Free-run counter (independent of processor)
Functions
  Input capture
  Output compare
  Pulse-width modulation (PWM) generation
  One-pulse mode output

## Slide 3: Timer: Clock
Reload Value
Timer
Counter
fCL_PSC
ISR
Interrupt
Reload
PSC
ARR
Prescaler
fCL_CNT
clock
Notes: A timer is a hardware component in ARM Cortex-M microprocessor. Each timer has a special register, which is called the timer counter. The counter runs freely. If enabled, it automatically counts upwards or downwards, under the driven of a clock source. Pay attention. It is hardware, not software, which keeps repeatedly incrementing or decrementing the counter value. For each rising edge in the clock signal, the value of the counter increments or decrements by one automatically. That is why, we say the counter of a timer, is the free-running counter.
By updating the PSC register, we set the timer to be clocked at the rate we desire. The PSC register holds the frequency pre-scaler value, or the frequency divider. The frequency of the clock source is divided by a constant integer, PSC plus 1, before the input clock is fed to the counter. The prescaler enables a tradeoff between timer resolution and timer range. High timer resolution requires a high clock rate. However, high clock rates cause the timer to overflow or underflow more quickly.

## Slide 4: Timer: Output
Reload Value
Timer
Counter
fCL_PSC
ISR
Interrupt
Reload
PSC
ARR
Prescaler
fCL_CNT
clock
Compare & Capture Register (CCR)
=
Timer Output
(OCREF)
Notes: When a timer is configured to generate an output signal, hardware constantly compares the freely-running counter, with a value stored in the compare and capture register (CCR). The output of the timer, OCREF, can be high or low, depending on the timer settings. Note that, when the function of a timer is output, the CCR register is used only for compare.

## Slide 5: Timer: Input Capture
Reload Value
Timer
Counter
fCL_PSC
ISR
Interrupt
Reload
PSC
ARR
Prescaler
fCL_CNT
clock
Compare & Capture Register (CCR)
Notes: A timer can also be used for input capture. When a specific external event occurs, such as a rising edge of an external signal on a G P I O pin, hardware automatically copies, the current value of the timer counter, to the compare and capture register (CCR). We can use such an ability to measure the timing information of a signal event, such as rising edge, or falling edge. By calculating the difference between two recorded CCR values, we can measure the period, or the pulse width of input signals. In this lecture, I will focus only on the output function, instead of the input capture. Specifically, I will show how to program the timer to generate a PWM signal.

## Slide 6: Multi-Channel Outputs
Notes: {{Pause=2}} Typically, a single timer can generate, up to 4 PWM signals, with independent duty cycles, and identical frequency. Each timer has four channels. Each channel has its own Compare and Capture Register. CCR1, CCR2, CCR3, CCR4. These four channels share the timer counter, and the auto-reload register (ARR). Therefore, these PWM outputs have exactly the same period. However, their duty cycle can be different, because the value of these CCR registers can differ from each other.

## Slide 7: Output Compare
Output Compare Mode (OCM) | Timer Output (OCREF)
000 | Frozen
001 | High if CNT == CCR
010 | Low if CNT == CCR
011 | Toggle if CNT == CCR
100 | Forced low (always low)
101 | Forced high (always high)

## Slide 8: PWM Mode
Mode | Counter < Reference | Counter ≥ Reference
PWM mode 1 (Low True) | Active | Inactive
PWM mode 2 (High True) | Inactive | Active

## Slide 9: Edge-aligned Mode (Up-counting)
ARR = 6, RCR = 0
clock
counter
Counter overflow
Update event (UEV)
Period = (1 + ARR) * Clock Period
= 7 * Clock Period
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Counter overflow
Counter overflow
Counter overflow
Notes: We can configure the timer to repeatedly count up, count down, or, count up and down. Let’s first take a look at the up-counting mode. The auto-reload register (ARR) holds the maximum counter value, which is also called the auto-reload value. The counter counts from 0 to the auto-reload value, then restarts from 0, and generates a counter overflow event. This figure shows an example of the counter behavior when ARR is 6, and the repetition counter is not used. In the up-counting mode, the counter rolls over and is reset when it exceeds 6. When the counter resets, it triggers a counter overflow and an update event (UEV). After that, a new period starts. The counting period is determined by the auto-reload value, as well as the clock period.

## Slide 10: Edge-aligned Mode (down-counting)
ARR = 6, RCR = 0
Clock
Counter
Period = (1 + ARR) * Clock Period
= 7 * Clock Period
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Counter underflow
Counter underflow
Counter underflow
Counter underflow
Update event (UEV)
Notes: In the down-counting mode, the counter counts from the auto-reloaded value down to 0. After the counter has reached 0, hardware automatically reloads the counter with the auto-reloaded value, and generate a counter underflow event and an update event (UEV). The counting period of the down-counting mode is exactly the same as the counting period of the up-counting mode.

## Slide 11: Center-aligned Mode
ARR = 6, RCR = 0
Clock
Counter
Update event (UEV)
0
1
2
3
4
5
6
0
1
2
3
4
5
1
2
3
4
5
6
0
1
2
3
4
5
Counter overflow
Counter overflow
Counter underflow
Counter underflow
Period = 2 * ARR * Clock Period
= 12 * Clock Period
Notes: In center-aligned mode, the counter counts from 0 to the auto-reload value minus 1, generates a counter overflow event, then counts from the auto-reload value down to 1 and generates a counter underflow event. Then it restarts counting
from 0. In this mode, the counting direction changes automatically on counter overflow and underflow.

## Slide 12: PWM Mode 1 (Low-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Upcounting mode, ARR = 6, CCR = 3, RCR = 0
Clock
Counter
CCR = 3
Period = (1 + ARR) * Clock Period
= 7 * Clock Period
Duty Cycle =
CCR
ARR + 1
=
3
7
OCREF
Timer Output =
High if counter < CCR
Low if counter ≥ CCR
Mode 1
Notes: A single timer can generate up to 4 PWM signals with independent duty cycles and identical frequency. When multiple PWM signals are generated by the same timer, all rising edges occur at the same time. That is why it is called edge-aligned.

## Slide 13: PWM Mode 2 (High-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Upcounting mode, ARR = 6, CCR = 3, RCR = 0
Clock
Counter
CCR = 3
Period = (1 + ARR) * Clock Period
= 7 * Clock Period
Duty Cycle = 1 -
CCR
ARR + 1
=
4
7
OCREF
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
Mode 2

## Slide 14: PWM Mode 2 (High-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Upcounting mode, ARR = 6, CCR = 3, RCR = 0
Clock
Counter
CCR = 5
Duty Cycle = 1 -
CCR
ARR + 1
=
2
7
Period = (1 + ARR) * Clock Period
= 7 * Clock Period
OCREF
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
Mode 2

## Slide 15: PWM Mode 2 (High-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
1
2
3
4
5
6
0
1
2
3
4
5
Center-aligned mode, ARR = 6, CCR = 3, RCR = 0
Clock
Counter
CCR = 3
Duty Cycle = 1 -
CCR
ARR
Period = 2 * ARR * Clock Period
= 12 * Clock Period
=
1
2
OCREF
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
Mode 2

## Slide 16: PWM Mode 2 (High-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
1
2
3
4
5
6
0
1
2
3
4
5
Center-aligned mode, ARR = 6, CCR = 3, RCR = 0
Clock
Counter
CCR = 1
Duty Cycle = 1 -
CCR
ARR
=
5
6
Period = 2 * ARR * Clock Period
= 12 * Clock Period
OCREF
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
Mode 2

## Slide 17: Auto-Reload Register (ARR)
Auto-Reload Preload Enable (ARPE) bit in TIMx_CR1
Preload Register
Auto-reload Register (ARR)
Write to ARR
Read from ARR
Triggered by Update Event (UEV)
ARPE = 1 (Syn Update)
ARPE = 0 (Asyn Update)
Auto-reload Register (ARR)
Write to ARR
Read from ARR
  If UDIS bit in TIMx_CR1 is 1, UEV event is disabled.
Notes: {{Pause=2}} The auto-reload register (ARR) can be updated synchronously, or asynchronously. If the A R P E bit in the timer CR1 register is 1, ARR will be updated synchronously. An update to ARR will be buffered in a register, named the pre load register. The contents of the pre load register, are transferred into ARR, when the next update event occurs. This update mechanism is synchronous to timer’s input clock, and timer’s output period. It prevents software from updating the output frequency or period, when the timer is still performing comparison operations. {{Pause=1}} On the other hand, if the auto-reload {{Pause=0.1}} pre load enable bit (A R P E), is 0, any updates to ARR will immediately take effect. This update mechanism is asynchronous, because the update does not take the clock timing information into considerations.

## Slide 18: Repetition Counter Register (PCR)
Notes: The update event (UEV) is generated with respect to the counter overflows and underflows. In fact, update events are only generated when the repletion counter has reached zero. When the repetition counter register (PCR) is zero, an update event is generated with respect to each overflow or underflow.

## Slide 19: Repetition Counter Register (PCR)
Notes: When the repetition counter register (PCR) is one, in Center aligned mode, the update event occurs either on the overflow or on the underflow depending on, when the RCR register was written, and when the counter was launched. If the RCR was written before launching the counter, the UEV occurs on the overflow. If the RCR was written after launching the counter, the UEV occurs on the underflow. In the upcounting mode, an UEV event is generated with respect to every other overflow. Similarly, an UEV event is generated every other underflow in the down-counting mode.

## Slide 20: Repetition Counter Register (PCR)
Notes: This shows the generation of UEV events when the repetition counter register (PCR) is two.

## Slide 21: Repetition Counter Register (PCR)
Notes: These are the UEV events when the repetition counter register (PCR) is three. An UEV is generated each 4th overflow or underflow event depending on when the RCR was written.

## Slide 22: Repetition Counter Register (PCR)

## Slide 23: PWM Output Polarity
Mode | Counter < CCR | Counter ≥ CCR
PWM mode 1 (Low True) | Active | Inactive
PWM mode 2 (High True) | Inactive | Active
 | Active | Inactive
Active High | High Voltage | Low Voltage
Active Low | Low Voltage | High Voltage
Output Polarity:
Software can program the CCxP bit in the TIMx_CCER register
Notes: {{Pause=2}} Software can program the polarity of PWM signals. Each timer has two PWM modes, mode 1 and mode 2. These two modes are complementary to each other. However, software can select the output polarity by writing the CCxP bit in the C C E R register. {{Pause=1}} Software can select either active high or active low. If it is active high, the output is high voltage for the active state, and low voltage for the inactive state. {{Pause=1}} On the other hand, for active low, the output is low voltage for the active state, and high voltage for the inactive state.

## Slide 24: Counting up, down, center

## Slide 25: Up-Counting: Left Edge-aligned
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Upcounting mode, ARR = 6, CCR = 3, RCR = 0
Clock
Counter
CCR = 3
OC1REF
CCR = 6
OC2REF
CCR = 3
CCR = 6
All rising edges occur at the same time!
PWM Period
Left-aligned
Notes: {{Pause=2}} In the up-counting mode, when multiple PWM signals are generated by the same timer, all rising edges occur at the same time. {{Pause=1}} That is why the up-counting mode is edge-aligned. This example shows the PWM output when CCR is 3 and 6. All rising edges of the PWM signals are aligned with the overflow events of the timer counter. {{Pause=1}} More specifically, the PWM outputs are left edge aligned, because all pulses are aligned to the left side of the PWM period. The outputs go to their active state at the beginning of the period, {{Pause=0.5}} stay on, for an amount of time determined by their duty cycle, {{Pause=0.5}} then turn off for the remainder of the period. After that, this process repeats. {{Pause=0.5}} In summary, If a timer is configured to count up, its PWM signals are edge-aligned, and more specifically, left-aligned.

## Slide 26: PWM Mode 2: Right Edge-aligned
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Upcounting mode, ARR = 6, CCR = 3, RCR = 0
CCR = 3
Clock
Counter
OC1REF
OC2REF
All falling edges occur at the same time!
CCR = 5
CCR = 5
CCR = 3
PWM Period
Right-aligned
Notes: {{Pause=2}} When multiple PWM signals are generated by the same timer in mode 2, all falling edges occur at the same time. That is why mode 2 is edge-aligned. This example shows the PWM output when CCR is 3, and 5. {{Pause=1}} All falling edges of the PWM signals are aligned with the overflow events. {{Pause=1.5}} More specifically, the PWM outputs are right edge aligned, because all pulses are aligned to the right side of the PWM period.

## Slide 27: PWM Mode 2: Center Aligned
Center-aligned mode, ARR = 6, CCR = 3, RCR = 0
0
1
2
3
4
5
6
0
1
2
3
4
5
1
2
3
4
5
6
0
1
2
3
4
5
CCR = 3
Clock
Counter
OC1REF
CCR = 1
OC2REF
PWM signals are center aligned!
CCR = 1
CCR = 3
PWM Period
Center-aligned
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
Notes: {{Pause=2}} When a timer generates multiple PWM signals, the centers of the PWM pulses are aligned with, the peak value of the timer counter. In other words, the active pulse of, all output channels, are placed at the center of each PWM period. {{Pause=2}} Center-aligned PWM signals are often used in electronic circuits, such as motor control and power supplies. The signals are symmetrical and thus have less harmonics. It helps reduce noise interference and power consumption.

## Slide 28: The devil is in the detail
Timer output control
Enable Timer Output
  MOE: Main output enable
  OSSI: Off-state selection for Idle mode
  OSSR: Off-state selection for Run mode
  CCxE: Enable of capture/compare output for channel x
  CCxNE: Enable of capture/compare complementary output for channel x
Notes: {{Pause=2}} The output of a timer is enabled by a combination of the following control bits: M O E (Main output enable bit), O S S I (Off-state selection for Idle mode), O S S R (Off-state selection for Run mode), C C x E (Enable of capture/compare output for channel x), and, C C x N E (Enable of capture/compare complementary output for channel x). {{Pause=0.5}} These control bits are located in the timer register C C E R, and register B D T R. {{Pause=1}} For example, in order to enable the output (O C) for channel x, we need to set the M O E bit to 1 in register B D T R. {{Pause=1}} Based on the need of software application, we can choose one of these three configurations.

## Slide 29: Input Capture
Monitor both rising and falling edge

## Slide 30: Input Capture
Monitor only rising edges or only falling edge

## Slide 31: Input Capture

## Slide 32: Input Filtering

## Slide 33: Input Capture Diagram

## Slide 34: Intro to the STEVAL Drone Kit:
The STEVAL-DRONE01 is a drone kit with fully functional open source code libraries

## Slide 35: The STEVAL Development Board
The drone uses the STEVAL-FCU001V1 development board, optimized for drone design

## Slide 36: General Purpose Input/Output (GPIO)
ARM Cortex-M4
FPU
D Bus
I Bus
S Bus
SRAM
FLASH
AHB Bus Matrix
APB Bus Matrix
GPIO B
GPIO C
GPIO D
GPIO A
GPIO F
GPIO G
GPIO H
GPIO E
STM32L4
Timer
SPI
UART
…
Notes: {{Pause=2}} The ARM Cortex-M4 processor core, is connected to the other components via three buses, include the data bus, the instruction bus, and the system bus. These buses are connected to the Advanced high performance bus (AHB) matrix. AHB is the backbone bus. It is used for high-performance, high clock frequency system modules, such as on-chip flash, on-chip SRAM, as well as G P I O modules. The chip also has a bridge that connects AHB to Advanced Peripheral Bus (APB). APB is for low bandwidth peripherals. APB connects most of the peripheral devices in the system, such as UART, S P I, and timer.
{{Pause=1}} Here is the basic structure of a G P I O module. I will explain the details of this module in the next slide.

## Slide 37: General Purpose Input/Output (GPIO)
ARM Cortex-M4
FPU
D Bus
I Bus
S Bus
SRAM
FLASH
AHB Bus Matrix
APB Bus Matrix
GPIO B
GPIO C
GPIO D
GPIO A
GPIO F
GPIO G
GPIO H
GPIO E
STM32L4
Timer
SPI
UART
…
Notes: {{Pause=2}} The ARM Cortex-M4 processor core, is connected to the other components via three buses, include the data bus, the instruction bus, and the system bus. These buses are connected to the Advanced high performance bus (AHB) matrix. AHB is the backbone bus. It is used for high-performance, high clock frequency system modules, such as on-chip flash, on-chip SRAM, as well as G P I O modules. The chip also has a bridge that connects AHB to Advanced Peripheral Bus (APB). APB is for low bandwidth peripherals. APB connects most of the peripheral devices in the system, such as UART, S P I, and timer.
{{Pause=1}} Here is the basic structure of a G P I O module. I will explain the details of this module in the next slide.

## Slide 38: Basic Structure of an I/O Port Bit Input and Output
Schmitt
trigger
Notes: {{Pause=2}} Most G P I O ports have 16 pins. This diagram shows the standard structure of one G P I O pin. It includes the basic structure for both digital input, and digital output. In this lecture, I will only focus on the digital output part. We will discuss the digital input in a separate lecture.

## Slide 39: Basic Structure of an I/O Port Bit: Output
Schmitt
trigger
Output Data Register
GPIO MODE Register
00 = Input, 01 = Output,
10 = AF, 11 = Analog (default)
GPIO Output Type Register (OTYPER)
0 = Output push-pull (default)
1 = Output open-drain
GPIO Pull-up/Pull-down Register (PUPDR)
00 = No pull-up, pull-down 01 = Pull-up
10 = Pull-down 11 = Reserved
Notes: {{Pause=2}} Here is the basic structure, that is designed for digital output, on one G P I O pin. There are four important registers related to output, including the output data register, {{Pause=1}} the mode register, {{Pause=1}} the data output type register, {{Pause=1}} and the pull-up pull-down register. In this slide, I only give a short overview of each registers. Detailed discussion will be presented in the next few slides. {{Pause=1}} We can use the mode register to configure the pin as output. {{Pause=1}} The output type register, sets the output pin as, either push-pull or open-drain. {{Pause=1}} The pull-up pull down register, specifies, whether the pin is pulled up to a high voltage by a resister, or the pin is pulled down to the ground via another resister.
{{Pause=1}} When the pin is configured as output, the value written to the output data register is output on the G P I O pin. {{Pause=1}} However, whether the pin has a high voltage output, a low voltage output, or a high impedance output, depends on the configuration of the output type register, and the pull-up pull-down register.

## Slide 40: Enable Clock
AHB2 peripheral clock enable register (RCC_AHB2ENR)
#define RCC_AHB2ENR_GPIOBEN ((uint32_t)0x00000002U)
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOBEN;
AND Gate
GPIOEN
Clock for Port B
SYSCLK
1
Notes: {{Pause=2}} To improve energy-efficiency, the clock of most peripherals, is turned off. As presented previously, the red LED is connected to the pin 2 of port B. {{Pause=1}} First of all, we need to enable the clock of G P I O Port B. The clock can be turned on or off by configuring the reset and clock control module (RCC). Specifically, the clock of port B is controlled by the AHB2, peripheral clock enable register (A H B 2 E N R). We need to set bit 1, that is, G P I O B Enable Bit, of this register to 1. When G P I O B Enable bit is 1, the clock signal can pass through this logic {{Pause=0.1}} AND gate to drive the port B. On the other hand, if G P I O B Enable it is zero, the output of the logic {{Pause=0.1}} AND gate is always zero. Accordingly, the port B has no clock input.
{{Pause=1}} Software can set G P I O B Enable bit to 1 by using bitwise OR. In order to make the code more readable, we use this macro to define this constant. In fact, this macro has already been defined in the device header file.

## Slide 41: GPIO Mode Register (MODER)
32 bits (16 pins, 2 bits per pin)
GPIOB->MODER &= ~(3UL<<4); // Clear bits 4 and 5 for Pin 2
GPIOB->MODER |= 1UL<<4; // Set bit 4, set Pin 2 as output
Pin 2
Pin 0
Pin 1
Notes: {{Pause=2}} Software can program each {{Pause=0.1}} G P I O pin as one of the following four different functions. First, digital input, which detects, whether an external voltage signal, is higher or lower than a predetermined threshold. Second, digital output, which controls the voltage on the pin. Third, analog functions, which perform digital-to-analog, or analog-to-digital conversion. Last, other complex functions, such as S P I data pin, and timer PWM output. We call the last category of functions as alternative functions. {{Pause=1}}
The function of a pin is controlled by the MODE register of this port. Each mode register has 32 bits. Port B has a total of 16 pins. The function of each pin is determined by two bits of the mode register. For example, bit 5 and bit 4 control the function of pin 2. When these two bits are zero zero, the pin is set as digital input. When these bits are zero one, this pin is used for digital output. When they are one zero, the pin has alternative function. Specific alternative function will be determined by the alternative function register of this port. When these two bits are one one, the pin will be used for analog-to-digital conversion (ADC), or digital-to-analog conversion (DAC). {{Pause=1}}
In this example, pin PB 2 will be used as output to turn on the red LED. Therefore, we need to set bit 5 and bit 4 to zero and one, respectively. {{Pause=2}} Here is the C code. First, we clear bit 4 and 5. Then we set bit 4 by using bitwise OR.

## Slide 42: GPIO Output Type Register (OTYPE)
16 bits reserved, 16 data bits, 1 bit for each pin
GPIOB->OTYPE &= ~(1UL<<2); // Clear bit 2
Notes: {{Pause=2}} Next, we need to set the output of mode of Pin 2 as push-pull, instead of open drain. Therefore, software has to clear bit 2 of the output type register. In the following few slides, I will explain what is the difference between push pull, and open drain.

## Slide 43: GPIO Input: Pull Up and Pull Down
A digital input can have three states: High, Low, and High-Impedance (also called floating, tri-stated, HiZ)
Pull-Up
Pull-Down
If external input is HiZ, the input is read as a valid HIGH.
If external input is HiZ, the input is read as a valid LOW.

## Slide 44: GPIO Output: Push-Pull
GPIO Output = 1
Source current to external circuit

## Slide 45: GPIO Output: Push-Pull
GPIO Output = 0
Drain current from external circuit

## Slide 46: GPIO Output: Open-Drain
GPIO Output = 0
Drain current from external circuit

## Slide 47: GPIO Output: Open-Drain
Output = 1
GPIO Pin has high-impedance to external circuit

## Slide 48: GPIO Output Speed
Output Speed:
  Speed of rising and falling
  Four speeds: Low, Medium, Fast, High
Tradeoff
  Higher GPIO speed increases EMI noise and power consumption
  Configure based on peripheral speed
    Low speed for toggling LEDs
    High speed for SPI
Low
Medium
Fast
High
Speed of Rising

## Slide 49: Slew Rate
Slew Rate:
Maximum rate of change of the output voltage
A high slew rate allows the output to be toggled at a fast speed.

## Slide 50: GPIO Output: Push-Pull vs Open-Drain
Output Bit | Push-Pull | Open-Drain
1 | High | HiZ
0 | Low | Low
Use push-pull output, instead of open-drain output!
Notes: {{Pause=2}} This table summarizes the difference between push pull, and open drain. Their difference is that, in the push-pull output, when the output data bit is one, the output pin has a high voltage. However, in the open-drain output, when the output data bit is one, the output pin is floating, or has high impedance. {{Pause=1}} In this example, we need to provide a high voltage on the output pin, in order to turn on the LED. Therefore, we have select the push-pull output, instead of the open-drain output.

## Slide 51: GPIO Output Data Register (ODR)
16 bits reserved, 16 data bits, 1 bit for each pin
GPIOB->ODR |= 1UL << 2; // Set bit 2
Pin 2
Notes: {{Pause=2}} The output data register is easy to understand. This register has the upper 16 bits reserved. It has 16 data bits, with one bit for each pin. Because the red LED is connected to pin 2, to turn on the LED, we need to set, bit 2, of the output data register, to 1.

## Slide 52: Light up the Red LED (PB.2)
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOBEN; // Enable clock of Port B
GPIOB->MODER &= ~(3UL<<4); // Clear mode bits
GPIOB->MODER |= 1UL<<4; // Set mode to output
GPIOB->OTYPE &= ~(1UL<<2); // Select push-pull output
GPIOB->ODR |= 1UL << 2; // Output 1 to turn on red LED
Notes: {{Pause=2}} This slide summarizes the software code, which can turn on the red LED. The red LED is connected to pin 2 of port B. The software involves four steps. First, we turn on the clock to enable port B. Then, we set the mode of pin 2 of port B as digital output. Next, we select push-pull output, instead of open-drain output. Finally, we set, bit 2, of the output data register to light up the red LED.

## Slide 53: GPIO Initialization
Turn on the clock to the GPIO Port (e.g. Port B)
  RCC->AHBENR |= RCC_AHBENR_GPIOBEN; Reset and Clock Control (RCC)
Configure GPIO mode, output type, speed, pull-up/pull-down
typedef struct
{
__IO uint32_t MODER;
__IO uint16_t OTYPER;
uint16_t RESERVED0;
__IO uint32_t OSPEEDR;
__IO uint32_t PUPDR;
__IO uint16_t IDR;
uint16_t RESERVED1;
__IO uint16_t ODR;
uint16_t RESERVED2;
__IO uint16_t BSRRL; /* BSRR register is split to 2 * 16-bit fields BSRRL */
__IO uint16_t BSRRH; /* BSRR register is split to 2 * 16-bit fields BSRRH */
__IO uint32_t LCKR;
__IO uint32_t AFR[2];
} GPIO_TypeDef;
#define PERIPH_BASE ((uint32_t)0x40000000)
#define AHBPERIPH_BASE (PERIPH_BASE + 0x20000)
#define GPIOB_BASE (AHBPERIPH_BASE + 0x0400)
#define GPIOB ((GPIO_TypeDef *) GPIOB_BASE)

## Slide 54: GPIO AFR:
The GPIO alternate function mode allows for each pin to perform a specialized task.
The tasks that can be performed vary from pin to pin, and include specific functions for various peripherals
The Alternate Function Register (AFR) is used to choose which Alternate Function each pin performs

## Slide 55: STEVAL Board Features:
The STEVAL features an STM32F4 32-bit MCU with a variety of sensors and other peripherals
The sensors include a 3D accelerometer and gyroscope, a 3D magnetometer, and a MEMS pressure sensor
The STEVAL libraries use these sensors to allow for flight by adjusting the PWM output to the drone’s motors

## Slide 56: The Lab:
Lab 1 will have you configure a timer on the STEVAL
Timer 4 will be configured to produce a PWM output
The drone uses this output to drive its rotors
The lab’s objective is to configure the timer and PWM output, then measure that output

## Slide 57: The Lab: GPIOs
To complete this and future labs, you will need to configure GPIO (General Purpose Input/Output) pins
These pins are used by the STM32F4 to communicate with its peripherals and sensors
The GPIO registers, containing various settings, must be configured before the GPIOs can be used

## Slide 58: Configuring Registers
The various registers used to configure the GPIOs, timers, and other components, can be difficult to correctly configure
The STM32F4’s reference manual should be used for the labs in this course, as it contains useful tables that show the mapping of every register
This document can be found in the course Drive

## Slide 59: Configuring Registers in Code:
The following will explain how to configure registers through an example.
Assume that we want to set GPIO pin B6 to output mode:
First, we look in the reference manual to find the associated register, which happens to be the GPIOB_MODER register
The table shows that, to set pin B6 to output mode, we must set bits 13 and 12 to 0 and 1, respectively

## Slide 60: Configuring Registers in Code:
To configure the register this way, we first do:
GPIOB->OTYPER &= ~(3<<(2*6));
This sets both bits 12 and 13 to zero, which ensures that the following command will work correctly
GPIOB->OTYPER |= 1<<(2*6);
This will set bit 12 to 1, and leave bit 13 set to 0
Performing operations this way prevents the bits we are not interested in from being modified
If the first line of code is not present, and bit 13 contains a 1 to begin with, that 1 will remain after the second line, causing an incorrect configuration

## Slide 61: Things to do before Lab 1:
Before working on Lab 1, please install TrueStudio
The TrueStudio IDE will be used in all future labs
Also, please download the STEVAL project code
These resources can be found in the course Drive